## Slide 1
Center for Innovation in Jewish Education
DFRobot DFR1154
AI Camera
Quick Start & Assembly Guide
Firmware v3.1.4 | Arduino IDE 2.x | OpenAI Integration
Includes: Hardware Setup • Arduino IDE Config • Code Upload • Web Interface Guide • Process Flow

## Slide 2
What You Need — Parts & Prerequisites
CIJE | DFR1154 AI Camera Quick Start Guide
2 / 12
REQUIRED
DFR1154
AI Camera Module (ESP32-S3 + OV3660 + Mic + Speaker)
Arduino IDE 2.x
Download from arduino.cc/en/software
USB-A to USB-C cable
For power and code upload to the board
OpenAI Account
API key required — platform.openai.com
WiFi Network
2.4GHz network with SSID and password
Computer
Windows, macOS, or Linux with USB port
OPTIONAL (Recommended)
○ AI Camera Tripod / Mount Kit
○ Arduino UNO (for Serial Automation)
○ Mini Breadboard + jumper wires
○ MicroSD Card (up to 16GB) — for file storage
○ Small speaker with MX1.25-2P connector
Code Library Required
ArduinoJson by Benoit Blanchon Version 7.42 or newer required Install via: Arduino IDE > Tools > Manage Libraries

## Slide 3
Hardware Overview — DFR1154 Board Features
CIJE | DFR1154 AI Camera Quick Start Guide
3 / 12
OV3660 Camera
160° wide-angle, infrared capable
PDM Microphone
GPIO 38/39, I2S interface
MAX98357A Speaker
I2S amplifier, GPIO 45/46/42
IR Illumination
GPIO 47, for low-light imaging
ALS Sensor
LTR-308 ambient light (GPIO 8/9)
SD Card Slot
Up to 16GB, SPI interface
Type-C USB
Power input + code upload port
Gravity Connector
GPIO 43(TX)/44(RX) for Arduino

## Slide 4
GPIO Pin Reference Table
CIJE | DFR1154 AI Camera Quick Start Guide
4 / 12
Tip: Camera (SIOD=8, SIOC=9) shares I2C with ALS sensor. PDM mic (GPIO 38/39) shares I2S_NUM_0 with camera DMA — real-time audio+video simultaneously is not supported.

## Slide 5
Step 1 — Arduino IDE Setup
CIJE | DFR1154 AI Camera Quick Start Guide
5 / 12
Configure Arduino IDE 2.x before uploading firmware to the DFR1154:
A. Board Manager Setup
1
Open Arduino IDE > File > Preferences
2
Add Board URL:
arduino.esp8266.com/stable/package_esp8266com_index.json
(also add Espressif ESP32 URL)
3
Tools > Board Manager > Search "ESP32" > Install esp32 by Espressif Systems
Timeout fix (if install fails):
Edit: ~/.arduinoIDE/arduino-cli.yaml
Add: network:
connection_timeout: 600s
B. Board Configuration (Tools Menu)
Board: ESP32S3 Dev Module
USB CDC On Boot: Enabled
Flash Size: 16MB (128Mb)
Partition Scheme: 16M Flash (3MB APP/9.9MB FATFS)
PSRAM: OPI PSRAM
C. Install Required Library
Tools > Manage Libraries > Search:
"ArduinoJson" by Benoit Blanchon
Install version 7.42 or newer

## Slide 6
Step 2 — Code Configuration
CIJE | DFR1154 AI Camera Quick Start Guide
6 / 12
Open the firmware .ino file in Arduino IDE and configure these settings before uploading:
v3.x First-Run Setup Wizard (Recommended — No Code Editing Required)
1. Upload firmware as-is → 2. Power on — camera broadcasts WiFi: "AI-Camera-Setup" → 3. Connect phone/laptop to that network → 4. Browser opens config portal → Enter your WiFi & OpenAI API key
Alternative: Hardcode Credentials in .ino File
const char* ssid = "YourWiFiSSID"; // ~line 46 const char* password = "YourWiFiPassword"; // ~line 47 const char* OPENAI_API_KEY = "sk-proj-xxxxxxxxxxxxxxxxxxxx"; // Your OpenAI key // Save file > Verify (checkmark) > Upload (arrow) to DFR1154

## Slide 7
Step 3 — Upload Firmware & First Boot
CIJE | DFR1154 AI Camera Quick Start Guide
7 / 12
Upload to DFR1154
1
Connect DFR1154 to computer via USB-A to USB-C cable
2
In Arduino IDE: Tools > Port > Select the COM port for your camera
3
Click the Upload button (right arrow) in Arduino IDE
4
Wait for compilation and upload to complete (~2-3 minutes)
5
Open Tools > Serial Monitor, set baud to 115200
6
Watch for the IP address to appear in the serial output
Serial Monitor Output
====================================
ESP32-S3 OpenAI Interface v3.1.4
====================================
SD Card OK
Camera OK
PDM Microphone OK
Speaker OK
Connecting to WiFi...
WiFi connected
IP: 192.168.0.181
====================================
API Key status: Configured
Initialized counters: Images:0 Audio:0
Open the Web Interface
1. Note the IP address from Serial Monitor 2. Open a browser on the SAME WiFi network 3. Type the IP in the address bar: http://192.168.0.XXX

## Slide 8
Web Interface — Layout & Controls Overview
CIJE | DFR1154 AI Camera Quick Start Guide
8 / 12
LEFT PANEL — Camera & Controls
Pairing Workflow Banner Yellow bar shows current step in the image/audio/analysis workflow
Stop Stream / Start Stream Green button — toggles live camera video feed on/off
Capture Button Purple — takes a still photo and saves to SD card
Review Button Shows/previews the most recently captured image
LIVE Indicator Green dot — shows camera stream is active and broadcasting
Camera Preview Area Live MJPEG stream from the OV3660 wide-angle camera
RIGHT PANEL — Audio & Files
Audio Playback Bar HTML5 player — plays back recorded WAV audio files with controls
Record Button Red — starts/stops PDM mic recording (saves as REC_N.wav on SD)
Speaker Button Controls MAX98357A speaker for TTS playback
Image for Export Selected image to pair with audio prompt for OpenAI analysis
Audio for Export Selected audio file to send as Whisper transcription prompt
Image/Audio Files (Resources) Lists all files on SD card; Save to PC or Add to Export

## Slide 9
Web Interface — Analysis Controls & Results
CIJE | DFR1154 AI Camera Quick Start Guide
9 / 12
Send to OpenAI
Sends the export image(s) + audio prompt to GPT-4 Vision and Whisper. Results appear in the analysis text box and are spoken via TTS speaker.
Replay TTS
Re-plays the most recent text-to-speech audio response through the MAX98357A speaker without re-calling the OpenAI API.
Export Package
Downloads a ZIP file to your PC containing the image(s), audio prompt, and OpenAI response text from the analysis session.
OpenAI Analysis Results Box
The large text area below the video panel displays the GPT-4 Vision response after analysis. Results are automatically spoken through the speaker using OpenAI TTS. The response is also saved to the SD card in /analysis/[timestamp]/ folder for archiving.
Example prompt result: "I can see a circuit board with an ESP32-S3 microcontroller. The OV3660 camera module is visible in the upper left..."

## Slide 10
Usage Process Flow — Step by Step
CIJE | DFR1154 AI Camera Quick Start Guide
10 / 12
Standard workflow for capturing, analyzing, and archiving with the DFR1154 AI Camera:
1
Start
Stream
Click 'Start Stream' — camera begins live MJPEG feed
▶
2
Capture
Image
Frame your subject, click 'Capture' to save to SD card
▶
3
Record
Audio Prompt
Click 'Record', speak your question/prompt, click 'Stop'
▶
4
Add to
Export
Select image + audio from Resources, click 'Add to Export'
▶
5
Send to
OpenAI
Click 'Send to OpenAI' — analysis result spoken via speaker
After Analysis — Optional Steps:
▶ Replay TTS
Re-listen to AI response via speaker
⬇ Export Package
Download ZIP with image + audio + response
✕ Delete Files
Clean SD card files from Resources panel
↺ Reset & Repeat
Start new capture session with fresh prompts

## Slide 11
Optional: Arduino UNO Automation Agent
CIJE | DFR1154 AI Camera Quick Start Guide
11 / 12
Connect an Arduino UNO to the DFR1154 via the Gravity Serial connector to create automated AI workflows:
Wiring: Arduino UNO ↔ DFR1154
Arduino UNO
DFR1154 Gravity
Pin 2 (SoftSerial RX)
GPIO 43 (TX)
Pin 3 (SoftSerial TX)
GPIO 44 (RX)
GND
GND
3.3V or 5V
+ (power)
Serial API Commands
CAPTURE — Take a photo
ANALYZE — Send to OpenAI
SPEAK:text — Speak via TTS
STATUS — Get system state
Classroom Use Cases
Automated sorting robot: Arduino moves objects, camera identifies and classifies them
Smart door: motion sensor triggers capture + AI description announcement
Science lab: photograph experiments at timed intervals, AI provides analysis each time
Inventory system: Arduino scans items, AI camera identifies and logs them
Interactive game: physical buttons trigger AI-powered responses to visual prompts
Environmental monitor: periodic capture + AI analysis of plant/weather conditions

## Slide 12
Troubleshooting & Quick Reference
CIJE | DFR1154 AI Camera Quick Start Guide
12 / 12
⚠ Board not found / COM port missing
✔ Install CH340 or CP2102 USB driver. Try a different USB cable (some are charge-only). Press BOOT button while plugging in.
⚠ Upload fails: Brownout / timeout
✔ Set Flash Size: 16MB and Partition: 16M Flash (3MB APP/9.9MB FATFS) in Tools. Use a powered USB hub.
⚠ Camera stream not showing
✔ Ensure USB CDC on Boot is Enabled. Refresh browser. Camera and PDM mic share I2S — audio recording stops stream briefly.
⚠ OpenAI returns 401 / 403 error
✔ Check API key is correct and has billing enabled at platform.openai.com. Key must not have extra spaces.
⚠ TTS / speaker not working
✔ Check speaker wiring on SPK connector (MX1.25-2P). MAX98357A uses GPIO 45 (BCLK), 46 (LRCLK), 42 (DIN).
⚠ SD card not detected
✔ Reformat SD card as FAT32. Use a card 16GB or smaller. Re-seat the card. Check SD LED on board during boot.
DFRobot Wiki
Arduino IDE Download
OpenAI Platform
ESP32 Setup Tutorial