## Slide 1
STEM PROFESSIONAL DEVELOPMENT
DFR1154 AI Camera
Hands-On AI Integration
for the Classroom
DURATION
90 Minutes
FORMAT
Interactive Workshop
AUDIENCE
STEM Educators (20–30)
Powered by OpenAI | ESP32-S3 Platform | Arduino IDE

## Slide 2
Session Agenda
90-Minute Interactive Workshop
5 min
1. Introduction & Live Demo
Meet the team & see AI camera in action
0:00–0:05
10 min
2. Workshop Overview
Materials, resources & breakout objectives
0:05–0:15
15 min
3. First Breakout
Assemble hardware, configure IDE, load firmware
0:15–0:30
5 min
4. Check-In
Verify successful setup of all cameras
0:30–0:35
10 min
5. Web App Tour
Interface walkthrough & workflow demo
0:35–0:45
30 min
6. Second Breakout
Explore AI analysis, build classroom applications
0:45–1:15
15 min
7. Report-Out
Share discoveries & curriculum connections
1:15–1:30

## Slide 3
What is the DFR1154 AI Camera?
HARDWARE HIGHLIGHTS
ESP32-S3R8
Dual-core 240MHz + 8MB PSRAM
OV3660 Camera
160° wide-angle, infrared capable
PDM Microphone
Built-in I2S digital mic (GPIO 38/39)
MAX98357 Amp
I2S speaker output for TTS audio
SD Card Slot
Expandable media storage
16MB Flash
Ample firmware + asset storage
VIN 3.7–15V
Flexible power input
AI CAPABILITIES
GPT-4 Vision
Analyze captured images with AI
Whisper STT
Speech-to-text from PDM microphone
TTS Playback
OpenAI text-to-speech via speaker
Live Streaming
Real-time camera feed in browser
Gallery Manager
Timestamped SD card file system
Export Packages
Download analysis + media bundles
Serial API
Control external Arduino devices
DFRobot SKU: DFR1154 | ESP32-S3 AI Camera V1.0 | Firmware v3.1.4

## Slide 4
Materials & Requirements
REQUIRED HARDWARE
DFR1154 AI Camera Module (1 per participant)
USB-A to USB-C cable
Laptop (Windows, Mac, or Linux)
WiFi network with internet access
Optional: AI Camera Tripod Kit
Optional: Arduino UNO + mini breadboard
Optional: Small speaker (MX1.25-2P)
SOFTWARE SETUP
Arduino IDE 2.x (free download)
ESP32 board package by Espressif
ArduinoJson library v7.42+
ESP32S3 Dev Module configuration
USB CDC On Boot: Enabled
Flash Size: 16MB (128Mb)
PSRAM: OPI PSRAM
ACCOUNTS & KEYS
OpenAI account (platform.openai.com)
Personal OpenAI API key (sk-...)
Pre-loaded API credits recommended
WiFi SSID + password for your venue
Web browser (Chrome recommended)
GitHub account (optional, for source)
SD Card 8–32GB (FAT32 formatted)
Estimated Cost: DFR1154 ~$35 USD | OpenAI API ~$0.05–$0.10 per analysis | Arduino IDE: Free

## Slide 5
Resource Links
HARDWARE
→ DFRobot DFR1154 Product Page
→ DFR1154 Wiki & Documentation
→ Purchase on DFRobot Store
→ AI Camera Tripod Kit
SOFTWARE & IDE
→ Arduino IDE 2.x Download
→ ESP32 Board Package (Espressif)
→ ArduinoJson Library (Blanchon)
→ Random Nerd ESP32 Setup Tutorial
OPENAI APIs
→ OpenAI Platform (API Keys)
→ GPT-4 Vision Documentation
→ Whisper Speech-to-Text API
→ Text-to-Speech API
CURRICULUM & AI TOOLS
→ AI for K-12 Guidelines (AI4K12)
→ CS Unplugged AI Activities
→ MIT App Inventor AI Extensions
→ Code.org AI Curriculum
All links are clickable in the digital version of this presentation

## Slide 6
GPIO Pin Reference (DFR1154)
CAMERA (OV3660)
XCLK
5
Y9
4
Y8
6
Y7
7
Y6
14
VSYNC
1
HREF
2
PCLK
15
SIOD
8
SIOC
9
MICROPHONE (PDM)
PDM_CLK
38
PDM_DATA
39
SPEAKER (MAX98357)
BCLK
45
LRCLK
46
DIN
42
GAIN
41
MODE
40
SD CARD
MO
11
MI
13
SCLK
12
CS
10
OTHER
LED
3
IR
47
BOOT
0
TX
43
RX
44
SDA
8
SCL
9
Note: Camera & Audio share I2S_NUM_0 — they cannot run simultaneously. Use blocking recordWAV() to avoid conflicts.

## Slide 7
Arduino IDE Configuration
1
Add ESP32 Board URL
File → Preferences → Additional Boards Manager URLs:
https://raw.githubusercontent.com/espressif/arduino-esp32/gh-pages/package_esp32_index.json
2
Install ESP32 by Espressif
Tools → Boards Manager → Search "ESP32" → Install "esp32 by Espressif Systems"
If timeout occurs: set connection_timeout: 600s in arduino-cli.yaml
3
Select Board & Settings
Tools → Board: "ESP32S3 Dev Module" | Then configure:
USB CDC On Boot: Enabled | Flash Size: 16MB (128Mb)
Partition: 16M Flash (3MB APP/9.9MB FATFS) | PSRAM: OPI PSRAM
4
Install ArduinoJson Library
Sketch → Include Library → Manage Libraries → Search "ArduinoJson"
ArduinoJson by Benoit Blanchon | Version 7.42 or newer
5
Configure Credentials in Sketch
Open ESP32_AI_Camera_v3_1_0.ino — set at top of file (~lines 45–48):
ssid = "YourWiFiSSID"
password = "YourPassword"
OpenAI_API_Key = "sk-..."

## Slide 8
Breakout 1: Assembly & Setup
TIME: 15 MINUTES
TASK A: Hardware Assembly
1
Unbox DFR1154 camera module
2
If using tripod kit, attach mounting bracket
3
Connect USB-A to USB-C cable to your laptop
4
Verify board powers on (LED should light)
5
Open Arduino IDE on your laptop
TASK B: IDE & Firmware
1
Verify ESP32 board package is installed
2
Select Tools → Board: ESP32S3 Dev Module
3
Apply the 5 settings from previous slide
4
Open ESP32_AI_Camera_v3_1_0.ino sketch
5
Enter your WiFi SSID, password & API key
TASK C: Upload & Connect
1
Select correct COM port (Tools → Port)
2
Click Upload button (→) in Arduino IDE
3
Wait for upload: "Done uploading" message
4
Open Serial Monitor (115200 baud)
5
Note the IP address shown (e.g. 192.168.x.x)
SUCCESS GOAL: Open a web browser, enter the IP address, and see the AI Camera web interface!

## Slide 9
AI Camera Web Application Tour
Pairing Workflow: Capture image/audio → Save to Export → Send to OpenAI Agent
Camera Stream
LIVE button starts real-time stream. Use Stop Stream / Capture / Review buttons to control image capture. Images auto-saved to SD card as IMG_xx.jpg
Audio Controls
Record button captures from PDM mic (WAV format). Speaker button plays back TTS audio. Audio Playback Bar shows duration and playback controls.
Image & Audio Files
Image Files section lists all SD card JPEGs. Audio Files shows all WAV recordings. Use Add to Export, Save to PC, or Delete File buttons.
OpenAI Analysis
Send to OpenAI sends selected image+audio to GPT-4 Vision. Results appear in text area. Replay TTS re-plays the AI response. Export Package downloads all.
1. Start Stream
2. Capture Image
3. Record Audio
4. Add to Export
5. Send to OpenAI
6. Review Results
7. Export Package
Access the interface by opening a web browser and entering the IP address shown in the Arduino Serial Monitor.
Example: http://192.168.0.181 | Note: Browser may show "Not Secure" — this is expected (self-signed certificate)

## Slide 10
Breakout 2: AI Exploration & Classroom Design
TIME: 30 MINUTES
Guided Activities (choose 1–2):
Object ID Challenge
Point camera at common classroom objects. Ask:
"What is this object and how might it be used in a science lab?"
Contextual Prompting
Photograph a diagram or equation. Ask:
"Explain this concept to a 6th grader in 3 sentences."
Lab Safety Check
Photograph a lab setup. Ask:
"Identify any potential safety concerns in this image."
Multi-Image Analysis
Capture before/after images of an experiment. Ask:
"Compare these two images and describe what changed."
Audio + Vision Combo
Record a verbal question, then capture an image. Have the AI respond to the spoken question about the visual.
Design a Lesson
Sketch how you would integrate this camera into ONE specific lesson or lab activity for your students.
Reflection: What subject area, grade level, and learning objective would this best support?

## Slide 11
Classroom Activity: Science Lab Observation
GRADE LEVEL
6–10
SUBJECT
Science / Biology
DURATION
45–60 min
AI FEATURE
GPT-4 Vision + TTS
ENGAGE
5 min
Teacher captures image of a biological specimen or plant using the AI camera. Projects the AI-generated description on screen to spark curiosity and discussion.
EXPLORE
15 min
Student groups take turns photographing specimens or lab materials. Each group verbally poses a scientific question about their specimen using the mic.
EXPLAIN
15 min
Groups send their image+audio to OpenAI. The AI response is read aloud via TTS. Students compare AI explanations with their own prior knowledge and textbook.
EVALUATE
10 min
Each group exports their analysis package (image + audio + AI response). They write a 3-sentence reflection comparing the AI answer to what they learned.
NGSS Aligned: MS-LS1, HS-LS2 | Supports: Asking Questions, Analyzing Data, Constructing Explanations

## Slide 12
Classroom Activity: Visual Problem Solving
GRADE LEVEL
7–12
SUBJECT
Math / Engineering
DURATION
50 min
AI FEATURE
GPT-4 Vision + Whisper
SETUP
Each pair of students gets a printed math problem or engineering design challenge
One student photographs the problem with the AI camera
Other student verbally states what approach they would try (mic recording)
AI ANALYSIS
Pair sends image + voice to OpenAI with prompt: "Solve this step by step, then explain your reasoning"
AI response is spoken via TTS — students listen without looking at the text
Students record key steps they heard in their science journal
CRITICAL COMPARISON
Students then read the full AI text response and compare to what they heard
Identify: Where was the AI correct? Where did they hear something different?
Discuss: Is the AI reasoning sound? What would you do differently?
EXTENSION
Change the prompt: "Solve this WITHOUT using algebra — use only visual/geometric reasoning"
Compare responses — discuss different problem-solving approaches
Export package for portfolio evidence of AI-assisted mathematical reasoning
Standards: CCSS MP.1, MP.3, MP.5 | NGSS Science & Engineering Practices | ISTE Standard 1.5

## Slide 13
AI in Education: Key Discussion Points
ACADEMIC INTEGRITY
When is AI use appropriate vs. not?
How do we teach responsible AI use?
Citation and attribution of AI-generated content
School/district AI use policies
EQUITY & ACCESS
Hardware cost considerations (~$35/unit)
API costs and budget planning
English Language Learner applications
Differentiated instruction opportunities
PEDAGOGICAL FIT
Best-fit subject areas and grade bands
Avoiding over-reliance on AI answers
Using AI to check student reasoning
Project-based learning integration
TECHNICAL LITERACY
Teaching how LLMs work (AI4K12)
Bias in AI-generated responses
Privacy considerations (images sent to API)
Prompting as a 21st century skill
"AI won't replace teachers — but teachers who use AI will replace those who don't."

## Slide 14
Report-Out: Share Your Learning
TIME: 15 MINUTES
Each group shares a 2-minute response to these prompts:
1
What subject, grade level, and lesson would you use this for?
2
What was the most surprising or useful AI response you received?
3
What student learning objective would this best support?
4
What challenge or concern do you have about classroom implementation?
5
What is your ONE next step to explore this further?
Facilitator: Capture key themes on whiteboard and note recurring ideas for follow-up resources

## Slide 15
Troubleshooting & FAQ
Q: Upload fails / no COM port
A: Enable USB CDC On Boot in Tools. Try different USB cable. Hold BOOT button while connecting.
Q: API key not working
A: Check no spaces/line breaks in key. Verify account has API credits. Key format: sk-....
Q: SSL Certificate error
A: Firmware uses insecure mode with encryption — this is intentional. "Not Secure" in browser is normal.
Q: No audio / mic not working
A: Camera and mic share I2S_NUM_0. Stop camera stream before recording. Audio requires 10x software amplification.
Q: SD card not found
A: Format as FAT32. DFR1154 uses SD_MMC. Ensure card inserted before power-up. Try <32GB card.
Q: Web interface freezes during analysis
A: Expected behavior — ESP32 is single-threaded. Periodic handleClient() calls provide updates. Wait 15–30 sec.
Q: "Boards manager" install timeout
A: Edit arduino-cli.yaml → add: network: connection_timeout: 600s → restart Arduino IDE.

## Slide 16
Next Steps & Resources
YOUR NEXT STEPS
Purchase your own DFR1154 camera (~$35)
Set up your OpenAI account & API key
Try the standalone firmware at home
Design ONE lesson that integrates AI vision
Share with your department or PLN
Explore the GitHub repository for source code
Join our follow-up session (date TBD)
KEEP EXPLORING
DFRobot Wiki — wiki.dfrobot.com/SKU_DFR1154
AI4K12 Framework — ai4k12.org
OpenAI Platform — platform.openai.com
Arduino IDE Download — arduino.cc/en/software
ESP32 Setup Tutorial — randomnerdtutorials.com
Code.org AI Curriculum — code.org/ai
ISTE AI in Education — iste.org/ai
Thank you for participating! Questions? Contact your CIJE facilitator.